Introduction to Vision and Robotics Coursework 2019-2020
By Emma Hughes (S1802886) and Cezar Mihalcea (S1736865)

Github Repository Link

https://github.com/cezarmihalcea/IVR

Vision

Discussion of Algorithms Used in Image Processing

[Discuss algorithms used for joint state estimation and target detection.]

Joint state estimation algorithms discussion. Need more detail on algorithmic specifics?

For joint state estimation, initially a trigonometric method was used but after that approach didn’t work, an inverse kinematic method was used. Thresholding was used to isolate the various last joint and effector, and then inverse kinematics was applied to work backwards to determine the angles.

For target detection, first a thresholding algorithm was used to isolate the pixels with colour in the specific range of the circle and square. Then a contouring algorithm was used to find the outline of each, then the number of vertices of each of the two shapes detected was compared – the one with more vertices is the sphere. From here, a distance measurement was taken relative to the base of the robot for each axis, these distances converted from pixels to metres, and then the overall distance was calculated using Pythagorean theorem.

Accuracy of Target Position Tracking and Sources of Error

[Plots of results for tracking target position vs actual position of target (10 tests) (one graph each for x, y and z).]

[Comment on sources of error in measurements.]

One possible source of error in the measurements is the effect of perspective – as the sphere moves further away from the camera, perspective causes it to appear slightly closer to the horizon than it actually is, thus making the measurement on the z axis too small at distance, and too large up close.

Another source of error that was encountered was that occassionally the identification algorithm would fail to distinguish between the square and the circle when the angle on the square was particularly awkward and would return the position of the circle instead.

Also, the pixel to metre conversion method is not exact, and this can result in slighty erroneous results.

The pinhole camera may also produce a distorted, pinhole effect, causing the image to be contorted in a manner that is not true to life, causing erroneous readings.

Robotics

Forward Kinematics Equation

[x,y,z]T = K(q)
q = [a,b,c,d]T
K = [(-3*cos(a+b+c)+3*cos(a-b+c)-3*cos(a+b-c)+3*cos(a-b-c)-2*cos(a+b+d)-2*cos(a-b+d)-cos(a+b+c+d)+cos(a-b+c+d)-cos(a+b-c+d)+cos(a-b-c+d)+2*cos(a+b-d)+2*cos(a-b-d)-cos(a+b+c-d)+cos(a-b+c-d)-cos(a+b-c-d)+cos(a-b-c-d)+6*sin(a+c)-6*sin(a-c)+2*sin(a+c+d)-2*sin(a-c+d)+2*sin(a+c-d)-2*sin(a-c-d))/4, (-6*cos(a+c)+6*cos(a-c)-2*cos(a+c+d)+2*cos(a-c+d)-2*cos(a+c-d)+2*cos(a-c-d)-3*sin(a+b+c)+3*sin(a-b+c)-3*sin(a+b-c)+3*sin(a-b-c)-2*sin(a+b+d)-2*sin(a-b+d)-sin(a+b+c+d)+sin(a-b+c+d)-sin(a+b-c+d)+sin(a-b-c+d)+2*sin(a+b-d)+2*sin(a-b-d)-sin(a+b+c-d)+sin(a-b+c-d)-sin(a+b-c-d)+sin(a-b-c-d))/4, (3*cos(b+c)+3*cos(b-c)+2*cos(b+d)+cos(b+c+d)+cos(b-c+d)-2*cos(b-d)+cos(b+c-d)+cos(b-c-d)+4)/2]T

Accuracy of Forward Kinematics

The accuracy of the forward kinematics equation was tested by comparing the calculated values for 10 different sets of joint angles by eye to the actual position assumed by the robot when the robot was moved into the corresponding pose. All 10 tests yielded good results – as best as could be determined, the end effector position was consistent with the coordinates provided.

Controller Accuracy and Sources of Error

[Plots of results for robot effector position vs target (10 tests) (one graph each for x, y and z).]

Possible sources of error include vision issues similar to those described in the sources of error for the target tracking – distortion due to perspective, distance, lenses, etc. - causing the joint measurements or target position tracking to be inaccurate.

Notably, this method relies on knowing the joint configuration of the robot – which cannot be determined uniquely from the pose of the robot – multiple joint settings could result in the exact same pose, entirely indistinguishable. Therefore, there is no guarantee that the joint angles measured were in fact the correct ones – they account for one possible configuration that would result in this pose. However, if this is not the correct configuration, then the inverse kinematics calculations could be adversely affected by this, even if the pose is the same.